Spherical Gridbox Volume
Volume of a spherical region bounded by surfaces of constant longitude, latitude and depth

---
Slice of data from a sphere
In our 2D sample the data is over a slice of
The globe which becomes thinner near the poles
Like a wedge slice taken out of a cantalope.
The amount of water represented by a gridcell
Is determined by the volume of the gridcell,
Therefore a volume-weighted average is appropriate.

---
Volume is a 3 dimensional integral
A gridbox in a three dimensional simulation in general is bounded by three pairs of surfaces with constant values of each one of the three coordinates respectively.
A gridbox in an ocean simulation using latitude-longitude horizontal coordinates, such as the one from which our sample data was extracted, in particular
Is bounded by two surfaces of constant depth(depth levels), two surfaces of constant latitude(surfaces along parallels) and two surfaces of constant longitude(surfaces along meridians).
One looks like a slightly curved box.
The volume of any region is equal to the integral of the constant unity(“1”) over that region.
For our gridbox the volume is the integral of unity over the bounds in depth, latitude and longitude.

---
Latlon ocean gridbox volume integral
If zmin,zmax are the gridbox bounds in depth
θmin, θmax are its bounds in latitude in radians, and
φmin,φmax are its bounds in longitude in radians,
Then the volume, V, of a latlon ocean model box is
V = ∫φminφmax ∫θminθmax ∫zminzmax 1 *[R2cos(θ)]dz dθ dφ
Where the term in square brackets is the area element factor for spherical coordinates and R is the radius of the sphere, the Earth in our case.
([R2cos(φ)] comes from considering an infinitesimal patch of the latitude longitude grid which is a rectangle with width of dφ times the radius Rcos(θ) of the small circle of the parallel the longitude range is an infinitesimal piece of, and height of dθ times the radius R of the great circle the latitude range is an infinitesimal piece of, hence (Rcos(θ)dφ)(Rdθ)=R2cos(θ)dθdφ .)

---
Gridbox volume integral simplifies
Since cos(θ) does not depend on R or φ and R2 does not depend on θ or φ the integral separates to
V = ∫φminφmax dφ ∫θmin θmax cos(θ) dθ ∫zminzmaxR2 dz
V = (φmax - φmin)(sin(θmax) – sin(θmin)) ∫zminzmaxR2 dz
Since the depth of the ocean is three orders of magnitude smaller than the radius of the Earth, most ocean models, including this one, take R to be constant so that this further simplifies to (with Δφ=(φmax - φmin)):
V = (sin(θmax) – sin(θmin))(zmax – zmin) Δφ R2

---
Volume weight
But though Δz=(zmax – zmin), the layer thickness, is a function of depth in our sample and most ocean models, Δφ is usually (and in our case) constant.
R2 is also taken constant.
For the purposes of weighting we can ignore all constant factors so the volume weighting is given by
weight = (sin(θmax) – sin(θmin)) Δz
The Δz , or z weighting, for our data is obtained by the thickness-weighted average program weitav1.m .
In a directory containing the file JAN1941sample
V = (sin(θmax) – sin(θmin)) Δz Δφ R2 , is the box volume
Which contains output from our model at a single column (a single latitude and a single longitude).

---
weitav1.m

---
Comments on weitav1.m
Note that the “load” command can be used to import data instead of the import wizard,
useful for importing data inside a matlab program.
Syntax: load <filename>
The thickness is calculated as the difference between the depth to the edge below and the depth to the edge above the data point.
The edges are mid-way between the data points, except for the top and bottom edges of the data which are 0 meters and 5000 meters respectively.
The “save” command can be used to export data,
This is also very useful.
To place an array into an ASCII file the syntax is
save <filename> <arrayname> -ASCII

---
Latitude weights
Once you have obtained the z weights, Δz(k),
From the zweight file produced by weitav1.m
It remains only to calculate the latitude weights and multiply to get the overall weights.
Although in many ocean models the latitude spacing is varied for physical reasons
In this one it is not, so the latitude points values are evenly spaced.
They are one degree apart.
The latitude in degrees of the center of the gridbox with latitude index j is -90.5 + j .
The latitude edges, θmax and θmin , for the gridbox with latitude index j are midway between the centers, except that for index 1, θmin is -90 degrees, the South Pole, and for index 180, θmax is +90 degrees, the North Pole.
For index 1 the center of the cell is equal to θmin .
For index 180 the center of the cell is equal to θmax .
From this you should readily be able to find the latitude weights.
In MATLAB
sin(theta)
Calculates the sine of theta in radians.
MATLAB functions cos and tan work analogously. (Don’t forget to convert from degrees to radians!).

---
HW #3
Write and run a matlab program weightave.m
to calculate riwtavg and khwtavg
the volume weighted averages of the Richardson number and Heat Diffusivity respectively over the ocean points
Of the slice of data in = JAN194110x2EoijlEsah6i_1l10x2Enc .
One must first calculate the volume of the gridcell corresponding to each data point,
Which will be the weight, w.